Caledonian Cables

Automotive Cable

AVSSX/AESSX

Application:

This XLPVC (XLPE) insulated single-core cable is used in electric system for automobile.

Construction:

Copper conductor

XLPVC(AVSSX)/XLPE (AESSX) insulation

Conductor: Cu-ETP1 bare or tinned according to JIS C3102

Insulation: XLPVC (AVSSX)

XLPE (AESSX)

Standard Compliance: JASO D 608-92

Technical Parameters:

Operating temperature:–40 癈 to +105 癈 (AVSSX)

Operating temperature:–40 癈 to +120 癈 (AESSX)

| AVSSX |
| --- |
|  | Conductor | Insulation | Cable |
| Nominal Cross- section | No. and Dia. of Wires | Diameter max. | Electrical Resistance at 20癈 max. | Thickness Wall nom. | Overall Diameter min. | Overall Diameter max. | Weight approx. |
| mm2 | No./mm | mm | mΩ/m | mm | mm | mm | kg/km |
| 1 x0.30 | 7/0.26 | 0.80 | 50.20 | 0.24 | 1.40 | 1.50 | 5 |
| 1 x0.50 | 7/0.32 | 1.00 | 32.70 | 0.24 | 1.60 | 1.70 | 7 |
| 1 x0.85 | 19/0.24 | 1.20 | 21.70 | 0.24 | 1.80 | 1.90 | 10 |
| 1 x0.85 | 7/0.40 | 1.10 | 20.80 | 0.24 | 1.80 | 1.90 | 10 |
| 1 x1.25 | 19/0.29 | 1.50 | 14.90 | 0.24 | 2.10 | 2.20 | 15 |
| 1 x2.00 | 19/0.37 | 1.90 | 9.00 | 0.32 | 2.70 | 2.80 | 23 |
| 1 x0.3f | 19/0.16 | 0.80 | 48.80 | 0.24 | 1.40 | 1.50 | 2 |
| 1 x0.5f | 19/0.19 | 1.00 | 34.60 | 0.30 | 1.60 | 1.70 | 7 |
| 1 x0.75f | 19/0.23 | 1.20 | 23.60 | 0.30 | 1.80 | 1.90 | 10 |
| 1 x1.25f | 37/0.21 | 1.50 | 14.60 | 0.30 | 2.10 | 2.20 | 14 |

www.caledonian-cables.co.uk	www.addison-cables.com	33

Caledonian Cables

Automotive Cable

| AVSSX |
| --- |
|  | Conductor | Insulation | Cable |
| Nominal Cross- section | No. and Dia. of Wires | Diameter max. | Electrical Resistance at 20癈 max. | Thickness Wall nom. | Overall Diameter min. | Overall Diameter max. | Weight approx. |
| mm2 | No./mm | mm | mΩ/m | mm | mm | mm | kg/km |
| 1 x2f | 37/0.26 | 1.80 | 9.50 | 0.40 | 2.60 | 2.70 | 22 |
| AESSX |
| 1 x0.3f | 19/0.16 | 0.80 | 48.80 | 0.30 | 1.40 | 1.50 | 5 |
| 1 x0.5f | 19/0.19 | 1.00 | 64.60 | 0.30 | 1.60 | 1.70 | 7 |
| 1 x0.75f | 19/0.23 | 1.20 | 23.60 | 0.30 | 1.80 | 1.90 | 10 |
| 1 x1.25f | 37/0.21 | 1.50 | 14.60 | 0.30 | 2.10 | 2.20 | 14 |
| 1 x2f | 37/0.26 | 1.80 | 9.50 | 0.40 | 2.60 | 2.70 | 22 |

The "f" in the nominal size column indicates a flexible conductor with a finer wire diameter.

*Note: Other configurations, sizes, colors and length not specified herein are available upon request.

34	www.caledonian-cables.co.uk	www.addison-cables.com