Caledonian Cables

Automotive Cable

FLR6Y-B

Application and Description:

This FEP insulated low-tension automotive cable is used in motorcycles and other motor vehicles for starting ,charging,lighting,signal and instrument panel circuits.

Cable Construction:

Copper conductor FEP insulation

Conductor:Cu-ETP1 bare/tinned according to DIN EN 13602

Insulation:FEP

Standard:

ISO 6722 Class F Special properties: Good Thermal properties

Technical Parameters:

Operating temperature: �65癈 to +210癈

|  | Conductor Construction | Insulation | Cable |
| --- | --- | --- | --- |
| Nominal cross- section | No. and Dia. of Wires | Diameter of Conductor max. | Electrical resistance at 20癈 bare/tinned max. | Nominal thickness | Overall Diameter Min. | Overall Diameter Max. | Weight approx. |
| mm2 | No./mm | mm | mΩ/m | mm | mm | mm | kg/km |
| 1x 0.35 | 12/0.21 | 0.9 | 54.4/55.5 | 0.2 | 1.2 | 1.4 | 5 |
| 1x 0.5 | 16/0.21 | 1.0 | 37.1/38.2 | 0.22 | 1.4 | 1.6 | 6 |
| 1x 0.75 | 24/0.21 | 1.2 | 24.7/24.4 | 0.24 | 1.7 | 1.9 | 9 |
| 1x1 | 32/0.21 | 1.35 | 18.5/19.1 | 0.24 | 1.9 | 2.1 | 12 |
| 1x 1.5 | 30/0.26 | 1.7 | 12.7/13.0 | 0.24 | 2.2 | 2.4 | 17 |
| 1x 2.5 | 50/0.26 | 2.2 | 7.6/7.82 | 0.28 | 2.7 | 3.0 | 28 |
| 1x4 | 56/0.31 | 2.75 | 4.71/4.85 | 0.32 | 3.4 | 3.7 | 41 |
| 1x6 | 81/0.31 | 3.3 | 3.14/3.14 | 0.32 | 4.0 | 4.3 | 62 |

Note: Other configurations, sizes, colors and length not specified herein are available upon request.

30	www.caledonian-cables.co.uk	www.addison-cables.com